## Slide 1: Butanol Blends as Marine Fuels An Overview
Thomas Wallner Argonne National Laboratory
Seminar at IBEX The International BoatBuilders’ Exhibition & Conference
Louisville, KY October 3, 2012

## Slide 2: What is Butanol?
A four carbon alcohol (C4H9OH), colorless, neutral liquid of medium volatility with a characteristic banana-like odor.
Traditionally petrochemically derived - generally used to make other chemicals, or used as a solvent or an ingredient in formulated products such as cosmetics.
Butanol exists in four (4) different isomers:
The structure of the four (4) isomers of butanol in comparison to ethanol (a two carbon alcohol (C2H5OH))

## Slide 3: How is Butanol made?
Acetone-butanol-ethanol (ABE) fermentation is a commonly used process
Can be biologically derived from biomass in a fermentation process using microorganisms – Biobutanol
Biobutanol fermentation differs from bioethanol mainly in the use of bacteria
An existing ethanol plant can be converted to make butanol
Yield per acre (or bushel) of butanol is lower on a volumetric scale but equivalent on an energy scale

## Slide 4: Properties of Butanol - Overview
 | Gasoline (EEE) | Ethanol | 1-butanol | 2-butanol | 3-butanol | Iso-butanol
Composition (C,H,O) (% mass) | 86, 14, 0 | 52, 13, 35 | 65, 13.5, 21.5 | 65, 13.5, 21.5 | 65, 13.5, 21.5 | 65, 13.5, 21.5
RON | 97 | 107.4 | 98.3 | 106 | 105 | 105.1
MON | 88.3 | 88.2 | 84.4 | 92 | 89 | 89.3
Melting point (ºC) | - | -112 | -79.9 | -114.7 | 25.5 | -108
Energy content (MJ/kg) | 42.9 | 25.6 | 32.9 | 32.9 | 32.9 | 32.8
Density (kg/L) | 0.742 | 0.789 | 0.81 | 0.81 | 0.79 | 0.81
Energy content relative to gasoline (%) | - | 64 | 84 | 84 | 82 | 83
Solubility in water | <0.1 | Fully miscible | 7.7 |  |  | 7.6
High energy content = Range
High knock resistance = Performance
Low solubility = Simplified storage/transport

## Slide 5: Properties of Butanol – Phase Seperation
As water enters a boat fuel system containing ethanol-extended fuels, phase separation may occur creating an ethanol/water fuel mixture.
Butanol does not phase-separate (cylinder on the right)
Effect of adding 10% water by volume to 85% ethanol and 10% water by volume to 85% butanol

## Slide 6: Properties of Butanol – Energy Content of Blends
16 Vol-% Butanol in Gasoline is equivalent in energy content to 10 Vol-% Ethanol in Gasoline

## Slide 7: Butanol today

## Slide 8: Properties of Butanol - Summary
Less susceptible to phase separation means butanol could be successfully delivered in existing pipelines
Eliminates need for splash-blending
Least corrosive of alcohols
Higher energy content – can be blended into gasoline at higher percentages than ethanol (Butanol at 16 Vol-% is equivalent in gravimetric energy content to ethanol at 10 Vol-%)
Butanol is produced and used today

## Slide 9: Project Overview
  Sponsor: Department of Energy – Vehicle Technologies Program – Fuel Technologies
  Project partners
    Bombardier Recreational Products (BRP)
    Michigan Technological University (MTU)
    Argonne National Laboratory
  Project start: March 1, 2012
  Project duration: 12 months (Phase 1)

## Slide 10: Butanol Blends as a Marine Fuel An Overview
Thomas Wallner Argonne National Laboratory
Seminar at IBEX The International BoatBuilders’ Exhibition & Conference
Louisville, KY October 3, 2012