## Slide 1
Pressurized Portable Marine Fuel Tanks
Mark Riechers

## Slide 2: EPA Regulation §(1060.105 (c))
(c) Portable marine fuel tanks and associated fuel-system components must meet the following requirements:
(1) They must be self-sealing (without any manual vents) when not attached to the engines. The tanks may not vent to the atmosphere when attached to an engine.
(2) They must remain sealed up to a positive pressure of 34.5 kPa (5.0 psig); however, they may contain air inlets that open when there is a vacuum pressure inside the tank.
effective 01 Jan 2010

## Slide 3
Current Design
35kPa
EPA Regulation §(1060.105 (c))
Portable Tank Design Changes
-2kPa

## Slide 4
Diurnal Pump Intake
FR
FR
FR
Wall of tank provides reactionary force to draw volume into the tank. (Tank wall is functioning as a pump diaphragm/spring)
Cool air

## Slide 5
Diurnal Pump Exhaust
FR
FR
FR
Wall of tank provides reactionary force to expel liquid from tank. (Tank wall is functioning as a pump diaphragm/spring)
If hose or engine leak… Pumping Cycle Continues until tank is empty

## Slide 6
Tilted Engine Applications

## Slide 7
Dynamic “Trailering” Overflow Test
Determine Maximum Dynamic Inlet Pressure
Ref. Vapor Separator (Optimax)
Combined Tilt and Turn
Worst-Case Turn
Position test unit at 70° tilt and 30° turn.
Route clear vent hose to container for overflow capture
Fill float bowl completely full (overflow into vent hose)
Accelerate assembly per respective value above
Apply pressure, monitor overflow for “pop-off” value

## Slide 8
Rough Road Testing

## Slide 9
Transom Vertical Motion Time History, 25 MPH, RR XING
Rough Road Results

## Slide 10
Portable Fuel Tank
Rough Road Conclusions
100 mm of transom displacement
Visible Leakage from Carburetor at 7kPa (1psi)