## Slide 1: California Air Resources Board Evaporative Emission Proposal
John McKnight
IBEX
Miami Beach Convention Center
October, 13, 2009

## Slide 2: Presentations and Information
http://www.nmma.org/government/environmental/?catid=1798
jmcknight@nmma.org
202-737-9757
Are you on the evaporative emission contact list?

## Slide 3: Applicability and Implementation
CARB standards will only apply to vessels with SI engines > 40 hp
CARB standards will harmonize with EPA standards through MY 2013
CARB standards will be implemented for MY 2014

## Slide 4: Changes to the Draft Pleasure Craft Regulation
 | EPA Regulation | CARB Proposal
Applicability | All vessels | Vessels > 40 HP
Fuel Injection | N/A | Vessels > 40 hp
Fuel Hose Permeation | 15.0 g/m2/day @ 23C | Harmonized standard for under cowl fuel lines only; Fuel hose- 5.0 g/m2/day @ 40 C CE10 test fuel
Fuel Tank Permeation | 2.5 g/m2/day @ 40 C or 1.5g/m2/day @28 C | Harmonize with EPA test procedures and test temperatures 1.0 g/m2/day @ 28 C CE10 test fuel
Diurnal | 0.4 g/gal/day | Harmonize with EPA venting test procedure but set lower standard (0.25 g/gal/day)
Test Procedures | Tank – 28 C Hose – 23 C Diurnal Profile – 78- 90 F | Tank – 28 C Hose – 40 C Diurnal Profile – 78-90 F

## Slide 5: Changes to the Draft Pleasure Craft Regulation
 | EPA Regulation | CARB Proposal
Onboard Vapor Recovery | N/A | Currently investigating ORVR control
Implementation Schedule | 2009 – Hose 2012 – Tank 2012/2013 – Diurnal | MY 2014
Labeling | EPA specific label – may be combined with USCG capacity tag | Manufacturers may propose an alternate label under ARB discretion- CARB disagrees with the combined label.
Warranty | Require reporting of defective emissions related problems to 20 vessels | Require reporting of defective emissions related problems to 10% of production or 20 vessels (whichever is less)
Certification | Equipment builders use certified components for installation | Evaporative equipment Manufacturers certify and receive EO’s and OEM installs or OEM receives EO’s.